## Slide 1
FIT VN | A305 glue information

## Slide 2
Lot code : Glue List
A305 FIT VN | Material information
NO | Station | Process Station Name | Glue type | Machine q’ty | FIT PN | Shelf life (day) | Thawing time | Use time (H)
1 | GC01 | Dispense glue on Dummy wire | Loctite 401 | 3 | 903-0001-956 | 720 | 1 H | 168 H
2 | GC02 | Dispensing glue on 5x core wires | Loctite 438 Glue For Laser | 2 | 903-0001-925 | 720 | 1 H | 24 H
3 | GC03 | Dispense glue on trim ring & JACK side | Loctite 3542 glue | 4 | 903-0002-824-V | 180 | / | 8 H
4 | GC04 | Load Boot into glue dispensing fixture & dispense glue | Loctite 3542 glue | 2 | 903-0002-824-V | 180 | / | 8 H

## Slide 3
Glue BOX No. Barcode & Label principle：
外箱标签规则：
Remark:
1. This BOX barcode label used to check materials
2. Day, month and year code , between date code, FIT P/N and box serial number ( must not contain”_” ,“-” and spaces )
Right code：221026903-0001-92500001
Wrong code：221026-903-0001-925-001、221026_903-0001-925_001、221026 903-0001-925 001
3. Suppliers will release the glue BOX barcode & label according to the principle form that FIT has given.
YYMMDDP ··· PCCCCC
YYMMDDP···PCCCCC
FIT P/N
For example：If FIT P/N is 903-0001-925, then“ P···P ”=“903-0001-925”
Character size related to P/N size.
Date codeFor example：Year=2022， month=10，day=26，
Then “ YYMMDD ”=“ 221026 ”.
Encoding Principle：
Box serial number
For example：First case of parts,
Then “ CCCCC”=“ 00001”,
3
5 位流水码
2.1 A204 LOT NO Barcode proposal

## Slide 4
Glue LOT No. Barcode (GLUE TUPE) & Label principle(小包裝）：
Remark:
1. This barcode label used to check materials
2. Day, month and year code , FIT P/N and box serial number ( must not contain”_” ,“-” and spaces )
Right code：220928 903-0001-925 000011
Wrong code： 221026-090-0005-311V-00101、221026_090-0005-311V_00101、221026 090-0005-311V 00101
3. Suppliers will release the lot no barcode & label according to the principle form that FIT has given.
YYMMDDP ··· PCCCCCC
YYMMDDP···PCCCCCC
FIT P/N
For example：If FIT P/N is 903-0001-925, then“ P···P ”=“903-0001-925”
Character size related to P/N size.
Encoding Principle：
Box serial number
For example：First case of parts,
Then “ CCCCC”=“ 000011”,
Date code
For example：Year=2022， month=10，day=26，
Then “ YYMMDD ”=“ 221026 ”.
6 位流水码，带上BOX的流水码信息
2.4 A204 LOT NO Barcode proposal

## Slide 5
1. 针对胶水满箱数量小于36支：
正常包装使用一个箱码, 胶水单支按照36进制执行。
Example：
箱码: 260626090-0001-92500001
胶水单支： 260626090-0001-925000011
260626090-0001-925000012
260626090-0001-925000013
.....
260626090-0001-92500001A
260626090-0001-92500001Z
2. 针对胶水满箱数量多于36：
新增小包装，每个小包装等于一个小箱码,里面胶水单支按照36进制执行。
Example：
I. 箱子装100支胶水=>大箱外箱标签请参考（Label 管理作業辦法档案）
II. 里面胶水要分成4包（3包30支，1包10支）=>包外要贴上箱码标签
箱码: 260626090-0001-92500001
260626090-0001-92500002
260626090-0001-92500003
260626090-0001-92500004
胶水单支：
第一包里面：260626090-0001-925000011
260626090-0001-925000012
260626090-0001-925000013
.....
260626090-0001-92500001A
260626090-0001-92500001Z =>一共30 个码
第二包里面：
260626090-0001-925000021
260626090-0001-925000022
260626090-0001-925000023
.....
260626090-0001-92500002A
260626090-0001-92500002Z =>一共30 个码
第三包。。。。
标签规则详细&例如：

## Slide 6
标签规则详细&例如：
2.3 A204 LOT NO Barcode proposal
2. 针对胶水和其他物料满箱数量多于36：
新增小包装，每个小包装等于一个小箱码,里面胶水单支按照36进制执行。
Example：
I. 箱子装100支胶水=>大箱外箱标签请参考（Label 管理作業辦法档案）
II. 里面胶水要分成4包（3包30支，1包10支）=>包外要贴上箱码标签
箱码: 260626090-0001-92500001
260626090-0001-92500002
260626090-0001-92500003
260626090-0001-92500004
胶水单支：
第一包里面：260626090-0001-925000011
260626090-0001-925000012
260626090-0001-925000013
.....
260626090-0001-92500001A
260626090-0001-92500001Z =>一共30 个码
第二包里面：
260626090-0001-925000021
260626090-0001-925000022
260626090-0001-925000023
.....
260626090-0001-92500002A
260626090-0001-92500002Z =>一共30 个码
第三包。。。。
1. 针对胶水和其他物料满箱数量小于36支：
正常包装使用一个箱码, 胶水单支按照36进制执行。
Example：
箱码: 260626090-0001-92500001
胶水单支： 260626090-0001-925000011
260626090-0001-925000012
260626090-0001-925000013
.....
260626090-0001-92500001A
260626090-0001-92500001Z

## Slide 7
THE END